Pokey

Firefighting robot for Trinity-style competition.

Ideally would like to upgrade, simplest, shortest path, to get the robot working well

Flame detection via combo of IR LEDs (the ones that are best for Trinity) and Gameboy B&W camera running at hopefully 30fps and accessible via I2C

Navigation – ??
Wall avoidance – ??

- Probably Sharp IR sensors w/ A2D adapters.
- Dual wheel encoders – could easily do this via I2C to an ATtiny reading pulses.
- I2C to GB camera
- Ideally logging/telemetry/control via Xbee or other radio.
- Dual floor sensors, could also run off A2D
- Fan control (servo)
- Differential drive motor control (dual motors)

Right now using Orangutan LV-168 which has ideal motor drivers but ATmega168 may be a bit light on memory if things get too complicated. I ran out of memory last time. Although I can probably significantly optimize the code this time around. I could use an Baby Orangutan ATmega328P. Lots more pins. Need a baseboard, probably.

- Status LCD
  - I2C backpack
- Flame Detection
  - GB cam via I2C
  - Need to run GBcam at 10-30fps
- Motor control
  - Differential drive
  - Dual wheel encoders for feedback
- Direction control
  - Wheel encoders
  - Gyro ?
- Flame extinguishing
  - RC plane propeller and motor/gearbox
  - Fan controller – ESC?
  - Fan deployment? Or static mount?
- Wall avoidance/following
  - Sharp sensors?
  - On rotating array?
  - Mount sharp appropriate distance—how?
  - VCNL 4000 I2C, 10-150mm range, Adafruit, Sparkfun
  - Plain old IR LED/Phototrans pair?
- Command, control, and telemetry
  - Xbee?
  - Wifi?
  - Other RF modules?
- Power
  - BEC from ESC that runs the fan?
  - Separate ESC (Pololu 3.5A?)
  - 2S LiPo could run ESC/Fan/BEC versus mult batteries, boost regulators, etc., run motors at 5V and/or find 5V versions of the motors.

Would an RTOS be of any value?